## Slide 1
Processor Arch: Pipelined
Program optimization
MADE BY: Zhong Zhineng & You Zhenbang

## Slide 2
Processor Arch: Pipelined

## Slide 3
Pipeline Basics
What’s the change of throughput and latency respectively?

## Slide 4
Pipeline Basics

## Slide 5
Pipeline Basics
Limitations of pipelining
  Nonuniform partitioning
  Diminishing Returns of Deep Pipelining
Number of pipeline stages of modern CPU
  AMD Zen2(3th Gen Ryzen): 19 stages
  Intel Ice Lake(10th Gen core): 14-19 stages

## Slide 6
SEQ->SEQ+

## Slide 7
Adding pipeline registers
Since valP is only used in the Memory period of call and in the Execute period of jXX and both of them do not need valA, Select A module is used to reduce the number of registers.
SEQ+->PIPE-

## Slide 8
Problems: Data/Control Dependency
Data hazard
Control hazard
(if there were no bubbles)

## Slide 9
A Simple Solution: Bubbles and Stalls
Handling data hazard
Handling control hazard

## Slide 10
Problem: Need the data that has not written back to the registers when decoding
Another solution: Forward the data
Our principle: Try to use forward. If that fails, we can use stalls.
Another Solution: Forward

## Slide 11
Modified HCL: Select PC & Fetch
HCL:

## Slide 12
Modified HCL: Decode/Write back
HCL:
Pay attention to the order.

## Slide 13
Modified HCL: Execute
HCL:

## Slide 14
Modified HCL: Memory
HCL:

## Slide 15
Hazard: Load/Use
上一条指令从内存读入寄存器（Memory阶段读出），本条指令需要用寄存器中的值
只转发做不到，只能暂停流水线，插入一个气泡，同时从Memory阶段转发到Decode
—— You cannot only use forwarding to solve all the problems.

## Slide 16
Hazard: ret
ret指令后一条指令的PC需要到Memory阶段才知道
解决方案：暂停流水线，插入三个气泡

## Slide 17
Hazard: Branch Misprediction
执行完Execute阶段就可以知道正确分支（Cnd）
解决方案：暂停流水线，插入两个气泡

## Slide 18
Hazard Combination

## Slide 19
Hazard Detection & Control

## Slide 20
Implementing Pipeline Control

## Slide 21
Program optimization

## Slide 22
Optimization
编译器可以进行的优化：
代码移动，比如将循环中相同重复计算提取到循环外
移位加减等代替乘除
部分表达式的复用
编译器必须保守而不能进行的优化：
过程调用可能有副作用
指针可能具有别名

## Slide 23
Simple Out-of-order Processor
In-order issue
Out-of-order execution
In-order commit
CPI may be less than 1

## Slide 24
Modern CPUs
Out-of-order execution
Multiple issue
Dynamic scheduling
Speculative execution
  Advanced prediction mechanisms
Register renaming

## Slide 25
数据流图和关键路径
关键路径提供的只是一个下界
还受到功能单元的数量, 功能单元之间能够传递数据值的数量影响

## Slide 26
Loop Unrolling

## Slide 27
Loop Unrolling with Separate Accumulators

## Slide 28
Loop Unrolling with Reassociation

## Slide 29
Notes
太多次展开会导致寄存器溢出
改变运算顺序的循环展开重新结合不可以用于浮点数(浮点数不满足结合律)

## Slide 30
Thanks for
your listening.